## Slide 1
B.TECH CE • SEMESTER VI • PROJECT
Adaptive TCP Congestion Control
using Deep Reinforcement Learning
PRESENTED BY
Jewel Bhannvadiya
CE-065
Archi Patel
CE-087
Henil Suchak
CE-148
GUIDED BY
Prof. Bhavika M. Gambhava
SUBJECT
System Design Practice (23CE625)
Department of Computer Engineering
Dharmsinh Desai University

## Slide 2
Agenda
What we'll walk through today
Adaptive TCP Congestion Control using Deep RL
2 / 27
01
Problem & Motivation
Why congestion control matters today
02
TCP Fundamentals
cwnd, RTT, packet loss in plain terms
03
Limitations of Classical Algorithms
CUBIC, Reno and their blind spots
04
Reinforcement Learning Approach
Mapping TCP to an MDP
05
Soft Actor-Critic (SAC)
Why this algorithm and how it learns
06
System Architecture
ns-3 • Python • Spring Boot • React
07
Implementation Details
Shared memory, training, reward design
08
Live Dashboard Demo
Real-time monitoring of SAC vs CUBIC
09
Conclusion & Future Work
What we achieved and what's next

## Slide 3
Problem Statement
The core challenge in TCP
Adaptive TCP Congestion Control using Deep RL
3 / 27
THE CORE QUESTION
“How fast should a sender transmit data without overwhelming the network?”
LIMITATIONS OF CLASSICAL ALGORITHMS
● Fixed rules: CUBIC / Reno use hand-tuned formulas
● React, don't predict: only respond after packet loss
● Single signal: loss is the only input used
● Static: one algorithm fits every network type
● Loss-blind: can't tell random loss from congestion
OUR GOAL
Learning-based adaptive controller
● Learns from experience, not hand-coded rules
● Uses multiple signals: RTT, throughput, cwnd, loss
● Adapts in real-time to changing conditions
● Robust against non-congestion packet loss

## Slide 4
Why Does This Matter?
Poor congestion control hurts real users every day
Adaptive TCP Congestion Control using Deep RL
4 / 27
📺
Video Streaming
Buffering, quality drops
📞
Video Calls
Latency spikes, stutter
🎮
Online Gaming
Lag, disconnections
⬇
Large Downloads
Wasted bandwidth
🏢
Data Centers
Incast collapse
📡
5G / Satellite
Highly dynamic links
KEY INSIGHT
Networks today are highly diverse — 5G, satellite, Wi-Fi, data-center fabrics.
A single fixed rule cannot perform optimally across all of them.

## Slide 5
Background — What is TCP?
The protocol that carries most of the internet
Adaptive TCP Congestion Control using Deep RL
5 / 27
Reliability
Lost packets are retransmitted
Ordering
Packets arrive in sequence
Flow Control
Don't overwhelm the receiver
Congestion Ctrl
Don't overwhelm the network
THE KEY VARIABLE
Congestion Window (cwnd)
cwnd = bytes allowed “in flight” (sent but not yet acknowledged)
● cwnd grows on every successful ACK — sender can push faster
● cwnd shrinks on packet loss — sender must slow down
● The entire congestion-control game is: how to grow cwnd and how much to cut it on loss

## Slide 6
How Congestion Happens
Bottleneck links, finite queues, and packet loss
Adaptive TCP Congestion Control using Deep RL
6 / 27
Sender
(fast)
Router
(bottleneck link)
Queue fills up → packets drop
Receiver
(slow link)
WHAT THE SENDER OBSERVES
RTT rises
Packets queued → longer round-trip time
Loss appears
Queue overflows → router drops packets
Throughput stalls
Link saturated → no gain from sending faster

## Slide 7
Traditional Algorithms — Reno & CUBIC
Hand-tuned rules that have served us since 1990
Adaptive TCP Congestion Control using Deep RL
7 / 27
TCP Reno (1990)
Additive Increase / Multiplicative Decrease
● Increase: cwnd += 1 segment per RTT
● On loss: cwnd = cwnd / 2
● Simple, predictable sawtooth pattern
● Too slow on high-bandwidth × delay links
TCP CUBIC (Linux default, 2006)
cwnd grows as a cubic function of time since last loss
W(t) = C · (t − K)³ + W_max
● RTT-independent growth — fair across delays
● Fast recovery after loss
● Still reacts only after loss occurs
COMMON LIMITATION
Both react only AFTER loss — by then the queue is already full.

## Slide 8
The CUBIC Sawtooth Pattern
How cwnd behaves over time — and what's wrong with it
Adaptive TCP Congestion Control using Deep RL
8 / 27
cwnd
time
LOSS
LOSS
LOSS
CHARACTERISTICS
● Aggressive growth: cubic curve probes bandwidth fast
● Sharp drop: cwnd ×0.7 on every loss event
● Loss-triggered: only reacts after damage is done
● Loss-blind: can't tell random from congestion loss
● Bufferbloat: RTT rises steadily before each drop

## Slide 9
Why Reinforcement Learning?
TCP congestion control is a textbook sequential decision problem
Adaptive TCP Congestion Control using Deep RL
9 / 27
RL Concept | Meaning | TCP Mapping
Agent | Decision maker | The TCP sender
Environment | World the agent acts in | The network (ns-3)
State | What the agent observes | RTT, throughput, cwnd, loss
Action | What the agent does | Adjust cwnd (scale factor)
Reward | Scalar feedback signal | High throughput, low RTT, no loss
KEY ADVANTAGES
● Learns optimal behavior from experience
● Combines multiple signals, not just loss
● Can anticipate congestion — act before loss
● Generalizes to unseen network conditions
● Improves automatically with more data
THE INTUITION
Instead of hand-coding rules, the agent discovers them by trial and feedback.
Good actions raise reward; bad ones lower it. The policy drifts toward good.

## Slide 10
Our MDP Formulation
The exact state, action, and normalization we use
Adaptive TCP Congestion Control using Deep RL
10 / 27
STATE SPACE — 6 features, normalized to [0, 1]
Feature | Description | Max Value
cwnd | Congestion window (bytes) | 1,400,000
rtt_us | Round-trip time (µs) | 200,000
throughput | Bytes / second | 250,000
packetLoss | Loss count in interval | 100
segmentSize | TCP segment size (bytes) | 1,500
bytesInFlight | Outstanding unACKed bytes | 1,400,000
ACTION SPACE
Continuous factor ∈ [ 0.8, 1.2 ]
Scales cwnd by ±20 % each step —
smooth, scale-free control.
UPDATE RULE
new_cwnd = cwnd × action
Step interval: 10 ms (simulated time)
Normalization ensures every feature contributes on the same scale — without it, the larger-magnitude inputs (e.g. cwnd in bytes) would dominate the neural network and small-but-important features (e.g. loss count) would be ignored.

## Slide 11
Reward Function Design
A single scalar that balances throughput, latency and loss
Adaptive TCP Congestion Control using Deep RL
11 / 27
+
Throughput term
√(throughput / T_max)
Concave — diminishing returns stop the agent from being greedy
−
RTT penalty
((RTT − RTT_min) / 400k)² × 40
Quadratic — strongly discourages buffer bloat
−
Loss penalty
0.3 + 0.05 × loss
Cliff penalty — discrete, triggered on any loss event
+
Stability bonus
0.1 × Gaussian(cwnd ≈ BDP)
Nudges the policy toward the ideal operating point
FINAL REWARD =
+ throughput_term − rtt_penalty − loss_penalty + stability_bonus
The reward is computed every 10 ms and clipped to [−2, 1.1]. Over training the agent learns that keeping RTT low near the BDP gives a better return than greedily maximising raw throughput.

## Slide 12
Why Soft Actor-Critic (SAC)?
The right RL algorithm for continuous, safety-sensitive control
Adaptive TCP Congestion Control using Deep RL
12 / 27
Aspect | DQN | PPO | SAC ✓
Action Space | Discrete only | Both | Continuous
Sample Efficiency | Medium | Low (on-policy) | High (off-policy)
Exploration | ε-greedy | Stochastic | Entropy bonus
Training Stability | Sensitive | Stable | Very stable
Continuous Actions
cwnd factor ∈ [0.8, 1.2] — DQN cannot represent this.
Off-Policy Replay
Every experience is re-used many times — precious in simulation.
Entropy Exploration
Keeps the policy curious; prevents premature convergence.

## Slide 13
SAC Algorithm — Actor & Critic
Two neural networks cooperate to learn a good policy
Adaptive TCP Congestion Control using Deep RL
13 / 27
ACTOR (π) — “What to do”
● Input: current state (6 features)
● Output: distribution over actions (Gaussian)
● Trained: to produce high-Q, high-entropy actions
● At inference: takes the mean (deterministic)
CRITIC (Q) — “How good”
● Input: state + action
● Output: Q-value (expected long-term return)
● Trained: to minimise Bellman-equation error
● Twin Qs: two critics reduce over-estimation bias
SAC OBJECTIVE — Maximum-Entropy RL
J(π) = E [ Σₜ rₜ + α · H(π(· | sₜ)) ]
Reward + entropy bonus → stable learning and principled exploration

## Slide 14
Neural Network Architecture
Same backbone used for both actor and critic
Adaptive TCP Congestion Control using Deep RL
14 / 27
Input Layer
6 normalized features
6
Dense + ReLU
Fully connected, 256 units
256
Dense + ReLU
Fully connected, 256 units
256
Dense + ReLU
Fully connected, 128 units
128
Output Layer
Action mean + log std-dev
2
MODEL SPECIFICATIONS
Trainable parameters
≈ 200,000
Activation
ReLU (hidden), tanh (output)
Framework
PyTorch via stable-baselines3
Optimizer
Adam, lr = 3 × 10⁻⁴
Discount factor γ
0.99
Replay buffer size
1,000,000
Mini-batch size
256

## Slide 15
System Architecture
Four cooperating layers, each with a specific job
Adaptive TCP Congestion Control using Deep RL
15 / 27
REACT DASHBOARD
Live charts — RTT, Throughput, cwnd, Reward
Port 3000 • Recharts • WebSocket client
▲ STOMP / WebSocket (real-time push)
SPRING BOOT BACKEND
REST API • H2 persistence • STOMP broadcast
Port 8080 • Java 17 • /topic/metrics
▲ HTTP POST /api/metrics (JSON)
PYTHON AGENT
Loads SAC model • inference loop • posts metrics
stable-baselines3 • PyTorch • 10 ms step
▲ Shared memory (ns3-ai, SHM id 2333)
NS-3 SIMULATOR
Dumbbell topology • TCP state machine • tracing
C++ 17 • ns-3.35 • ns3-ai shared memory

## Slide 16
Network Topology
Classical dumbbell — both algorithms share the bottleneck
Adaptive TCP Congestion Control using Deep RL
16 / 27
SAC Sender
(Node 2)
CUBIC Sender
(Node 3)
Router 0
Router 1
SAC Sink
(Node 4)
CUBIC Sink
(Node 5)
2 Mbps / 20 ms / FqCoDel 100p
10 Mbps / 20 ms
10 Mbps / 20 ms
Bottleneck
2 Mbps / 20 ms
Access link
10 Mbps / 20 ms
Base RTT
≈ 80 ms
BDP
≈ 2,500 bytes

## Slide 17
Shared Memory Communication
Why ns-3 and Python must talk at sub-millisecond speed
Adaptive TCP Congestion Control using Deep RL
17 / 27
Method | Round-trip Latency | Fit for 10 ms steps
TCP Socket (localhost) | ~10 µs | Marginal
gRPC | ~50 µs | Acceptable
Shared Memory (ns3-ai) | ~100 ns | Optimal ✓
LOCK-STEP EXCHANGE (every 10 ms)
1
C++ writes observation
struct sTcpRlInferenceEnv
2
Python reads obs, runs SAC
model.predict(state)
3
Python writes action
struct TcpRlInferenceAct
4
C++ reads, updates cwnd
tcb->m_cWnd = new_cwnd
Packed C struct shared with Python (ctypes)
struct sTcpRlInferenceEnv {
uint32_t cWnd;
int64_t rtt_us;
double throughput;
uint32_t packetLoss;
uint32_t segmentSize;
uint32_t bytesInFlight;
/* ... */
} Packed;
Synchronisation: POSIX condition variable → producer-consumer rendezvous every step

## Slide 18
Training Pipeline
Two-phase curriculum with reward refinement
Adaptive TCP Congestion Control using Deep RL
18 / 27
Phase 1 — Initial Training
● Steps: 2,000,000
● RTT penalty: linear (× 12)
● Goal: learn to maximise throughput
● Outcome: basic policy that keeps the link busy
Phase 2 — Fine-Tuning
● Steps: 200,000
● RTT penalty: quadratic (× 40)
● Goal: reduce buffer bloat, stabilise cwnd
● Outcome: latency-aware, production-ready policy
KEY TRAINING HYPER-PARAMETERS
Learning rate
3 × 10⁻⁴
Replay buffer
1,000,000
Batch size
256
Discount γ
0.99
Step interval
10 ms (sim)
WHY TWO PHASES?
Phase 1 teaches the agent to USE the link. Phase 2 teaches it to USE IT GENTLY.

## Slide 19
Experimental Setup
Reproducible head-to-head evaluation
Adaptive TCP Congestion Control using Deep RL
19 / 27
METHODOLOGY
● Simulation duration: 200 seconds per run
● Random seed: 42 (reproducibility)
● Runs per algorithm: 3 × averaged
● Metrics captured: Throughput, RTT, Loss, Reward
● Sampling rate: every 10 ms (SAC), 100 ms (CUBIC)
ALGORITHMS COMPARED
DRL-SAC
Our proposed learning-based controller
TCP CUBIC
Linux default — cubic growth
TCP NewReno
Classical AIMD baseline
TCP BBR
Google's model-based controller
EVALUATION SCENARIOS
① Baseline (no packet loss) ② With 0.1 % random packet loss
Same topology, same traffic pattern — only the congestion-control algorithm changes.

## Slide 20
Live Dashboard — Overview
Real-time monitoring of SAC and CUBIC side by side
Adaptive TCP Congestion Control using Deep RL
20 / 27
🖼 PASTE DASHBOARD SCREENSHOT HERE
(right-click → Change Picture)
⌘ Replace this placeholder with a screenshot of the running dashboard.

## Slide 21
Live Dashboard — SAC vs CUBIC Comparison
Throughput, RTT and cwnd trajectories
Adaptive TCP Congestion Control using Deep RL
21 / 27
🖼 PASTE DASHBOARD SCREENSHOT HERE
(right-click → Change Picture)
⌘ Replace this placeholder with a screenshot of the running dashboard.

## Slide 22
Technology Stack
One purpose-built tool per layer
Adaptive TCP Congestion Control using Deep RL
22 / 27
n
Simulation
ns-3 (C++)
Packet-level network simulation
n
IPC Bridge
ns3-ai (shared memory)
Sub-millisecond C++ ↔ Python
P
RL Agent
Python + stable-baselines3
SAC model training & inference
S
Backend
Spring Boot + H2
REST API, persistence, broadcasting
R
Frontend
React + Recharts
Live visualisation components
S
Realtime Protocol
STOMP over WebSocket
Pub / sub streaming to the browser

## Slide 23
Key Contributions
What this project uniquely delivers
Adaptive TCP Congestion Control using Deep RL
23 / 27
01
End-to-End Integration
Working SAC ↔ ns-3 pipeline via ns3-ai shared memory at 10 ms steps.
02
Two-Phase Training Pipeline
Initial throughput-focused training followed by latency-focused fine-tuning.
03
Loss-Robust Policy
Learns to distinguish congestion loss from random loss — a capability that classical algorithms lack.
04
Full-Stack Monitoring
Spring Boot backend + React dashboard stream live metrics for both SAC and CUBIC side-by-side.
05
Reproducible Research
Fixed seeds, documented hyper-parameters, and a consistent comparison framework.

## Slide 24
Limitations
Honest account of what this system does not yet solve
Adaptive TCP Congestion Control using Deep RL
24 / 27
⚠ Single Topology
Trained only on a 2 Mbps / 80 ms dumbbell — generalisation to other networks is untested.
⚠ Multi-Flow Fairness
Behaviour against many competing flows has not been systematically evaluated.
⚠ Residual Bufferbloat
RTT is still slightly above the physical baseline under heavy load.
⚠ Simulation-Only
The agent has not been validated on a real Linux kernel or hardware NIC.
⚠ Hand-Tuned Reward
Reward coefficients are fixed constants chosen by the authors, not learned.
⚠ No Online Adaptation
Inference uses a frozen model — it cannot self-correct after deployment-time drift.

## Slide 25
Future Work
Short-term improvements and long-term research directions
Adaptive TCP Congestion Control using Deep RL
25 / 27
Immediate Improvements
▸ Diverse topologies
Train across varying bandwidth, delay, queue sizes
▸ Multi-flow evaluation
Quantify fairness vs BBRv2, CUBIC, Reno mixes
▸ Real traces
Replay captured WAN / 4G packet traces
Advanced Research Extensions
▸ Recurrent / Transformer policy
Capture long-range temporal patterns
▸ Curriculum learning
Easy networks first, then harder ones
▸ Safe RL constraints
Bound worst-case RTT during exploration
▸ Linux kernel deployment
Export via eBPF / TCP_CONG hook

## Slide 26
Conclusion
What we demonstrated and why it matters
Adaptive TCP Congestion Control using Deep RL
26 / 27
✓
Deep Reinforcement Learning is a viable approach for TCP congestion control.
✓
A Soft Actor-Critic policy can match or exceed classical algorithms in normal conditions.
✓
The learned policy is significantly more robust when random packet loss is present.
✓
The agent learned to distinguish random loss from congestion — something classical algorithms cannot do.
BOTTOM LINE
Learning-based congestion control can adapt to network diversity that classical algorithms were never designed for.

## Slide 27
Thank You
Questions, critique, and discussion are welcome.
Adaptive TCP Congestion Control using Deep Reinforcement Learning
TEAM
● Jewel Bhannvadiya (CE-065)
● Archi Patel (CE-087)
● Henil Suchak (CE-148)
Guided by Prof. Bhavika M. Gambhava
Q & A